## Slide 1
Development and test of real-size MRPC for CBM-TOF
Outline:
  Introduction on FAIR and CBM-TOF
Development of low resistive glass
Design of strip-MRPC and pad-MRPC
Beam test @GSI and SPS
Conclusions
  Wang Yi for CBM-TOF group
Department of Engineering Physics, Tsinghua University

## Slide 2
SIS100/300
SIS18
HESR
CR
Compressed Baryonic Matter
Super Fragment-Separator:
Nuclear Structure and Astrophysics
Anti-Proton Physics
p-Linac
100 m
FAIR phase 1
FAIR phase 2
Atomic, Plasma, Applied Physics
Facility for Antiproton and Ion Research
Primary Beams
1012/s; 1.5 GeV/u; 238U28+
1010/s 238U73+ up to 35 GeV/u
3x1013/s 30 GeV protons
Secondary Beams
range of radioactive beams up to 1.5 - 2 GeV/u; up to factor 10 000 higher in intensity than presently
antiprotons 3 - 30 GeV

## Slide 3
Time of Flight
Projectile
Spectator
Detector
DAQ/FLES HPC cluster
(SIS100)
Dipol
Magnet
Silicon
Tracking
System
Micro
Vertex
Detector
Ring
Imaging
Cherenkov
Transition
Radiation
Detector
(SIS100)
Muon
Detector
(SIS100)
Layout of CBM detector

## Slide 4
The structure of CBM-TOF wall
CBM-ToF Requirements
Full system time resolution sT ~ 80 ps
Efficiency > 95 %
Rate capability  30 kHz/cm2
Polar angular range 2.5°– 25°
Occupancy < 5 %
Low power electronics
(~100.000 channels)
Free streaming data acquisition
Au+Au, Center, 10AGeV
Simulated with CBM ROOT

## Slide 5
Development of low resistive glass
Performance of the glass
Glass mass production
Yield >100m2/month
Aging test with X-ray source
Online test system. The efficiency and time resolution can be obtained by cosmic ray while irradiated by X-rays. 0.1C/cm2 charge is accumulated in 35 days.

## Slide 6
Rate: 70kHz/cm2
Time resolution: 40 ps
Rate capability of high rate MRPC
Even though the rate is 70kHz/cm2, the efficiency is still higher than 90% and the time resolution is about 80ps.
Test results at Nuclotron, Dubna

## Slide 7
Prototype design for CBM-TOF
Strip-MRPC
Pad-MRPC

## Slide 8
Design of inner wall based on pad-MRPC
Glass: 0.7mm, 5.2cm x 19.5cm
Pad: 2cm x 2cm, 16pads
Gas gap: 10 x 0.22mm

## Slide 9
9
Feature Module | Efficiency | Time resolution | Dark rate | Cluster size
MRPC_1 | 98.4% | 56.2 ps | 0.57 Hz/cm2 | 1.23
MRPC_2 | 98.6% | 58.7 ps | 0.53 Hz/cm2 | 1.30
MRPC_3 | 98.4% | 62.0 ps | 0.55 Hz/cm2 | 1.25
HV: 6.0kV
The reference time is about 62ps (2.48x25ps).
Cosmic test of pad-MRPC

## Slide 10
10
10
Glass: low resistive glass
0.7mm thick, 27cm x 25cm
Strip: 27cm x 0.7cm, 0.3cm interval, 24 strips
Gas gap: 8 x 0.25mm, two stacks
Gas box: 600mm x 500mm x 72mm
Design of strip-MRPC for high rate region
Differential strip: 7mm wide+3mm interval
h
w
t
ground
Feed trough: Micro-strip, 50Ω

## Slide 11
11
11
Experimental Setup:
Particle trajectory
Buc-2013
THU-Pad
Buc-Ref
PMT
HD-Ref
Beam time in October 2014 at GSI
1.1 GeV 152Sm beam On 0.3mm/4mm/5mm Pb target
Flux rate several hundreds Hz/cm2
THU-Strip
HD-P2
BEAM
Beam test @GSI, Oct.2014
Particle trajectory

## Slide 12
12
High rate test in February 2015 at SPS CERN
13 GeV Ar beam
Flux rate around 1kHz/cm2
Buc-2013
THU-Pad
Buc-Ref
PMT
HD-Ref
THU-Strip
HD-P2
Experimental Setup:
USTC
Up setting
Down setting
Beam test @ SPS Feb 2015

## Slide 13
The data analysis is based on CBM ROOT, macro developed by TOF Group.
Analysis Procedure: 3 Main Steps.
1
Unpacking
2
Cluster Building
3
Analysis
Converting LMD files into unpacked ROOT file, containing timing, TOT, super module type, super module, RPC, strip, side information of each hit.
Initial calibration: Align center of each strip in Detector Under Test and Reference Detector.
Iterative calibration: Calibrate data in time-walk, gain and velocity correction.
Build calibrated hits into clusters.
Calculating observables from fully calibrated hits include cluster size, time resolution and efficiency.
Data analysis method

## Slide 14
Calibration method
Time-walk correction
Gain correction
Strip alignment correction
Velocity correction
Large signals arrive at discriminator threshold faster, leading to a dependence of measured time and amplitude of the analogue signal.
Amplification gain of PADI varies between each channel, which should be corrected out to get initial amplitude for time-walk correction.
Different cable length and electronic delay lead to the shifting of calculated center of different strip, influencing the position of hits.
Slower particles need a longer time to cross the distance between Dut and Mref, widen the time difference distribution.

## Slide 15
15
Analysis Setting:
Particle
Lower part of setup:
Diamond
THU-Strip
HD-Ref
BRef:
Starting counter for events.
Dut:
Counter under test.
MRef:
Reference measure for Dut.
Analysis Procedure:
Init_calib.sh (Initial calibration)
Iter_calib.sh (Iterative calibration)
  iteration procedure: 1-6-8-2-10-2-10
Iter_hits.sh (Analysis)
  analysis correction procedure: 1-2-3-4-1
Cut Selection: Cut 1
tofAnaTestbeam->SetMul4Max(1.);
tofAnaTestbeam->SetCh4Sel(8.);
tofAnaTestbeam->SetDCh4Sel(7.); tofAnaTestbeam->SetPosY4Sel(0.5);
tofAnaTestbeam->SetMulDMax(1.); tofAnaTestbeam->SetDTDia(0.);
Analysis results: GSI Oct 2014

## Slide 16
Run: Sun1205 – 5500V: Analysis Process
Before Calibration
After Calibration
Time-walk correction
Velocity correction

## Slide 17
Run: Sun1205 – 5500V Time Resolution
Threshold | Efficiency | Time Resolution | Cluster Size
170mV | 97.0% | 71.6ps | 1.7
180mV | 97.0% | 68.9ps | 1.7
190mV | 97.0% | 71.0ps | 1.6
200mV | 96.7% | 68.9ps | 1.6
Analysis Result under Different Threshold
Efficiency:
Around 97%
Time resolution:
Around 70ps
Results of strip-MRPC

## Slide 18
We Plot Y: (ThuPad tdc - BucRef tdc) vs X: (ThuPad tdc –RefTdc(fastest diamond tdc)) and Y: (BucRef tdc - ThuPad tdc) vs X: (BucRef tdc – RefTdc)
FitSlicesY() for these plots, then fit the mean value of each bin with a function, fun = pol 0+pol 1, and correct every BucRef tdc with BucRef tdc ‘ = tdc – fun->Eval(ThuPad tdc –BucRef tdc)
Velocity correction for pad-MRPC

## Slide 19
Time resolution of Pad-19
Time resolution of 5 pads
Efficiency: 98.8% @6kV
Results of pad-MRPC

## Slide 20
All events
Single-hit event for Thu-Pad
Single-hit event for BucRef
Single-hit event for BucRef and Thu-Pad
Single-hit event study
An overall time resolution of is obtained
Compared to strip-MRPC, pad-MRPC suffers less from multi hit events

## Slide 21
Choose event with Pad hits, count number of fired pads in this event: if nPadHits==1, single hit. If nPadHits>1, loop all fired pads, only record the pads with other fired pads near it.
Average cluster size: 1.7
Cluster size

## Slide 22
Performance | Strip-MRPC | Pad-MRPC
HV | 5.5kV | 6kV
Efficiency | 97% | 98.8%
Time resolution | 49ps | 62ps
Cluster size | 1.7 | 1.7
Conclusions
Both strip-MRPC and pad-MRPC meet the requirement of CBM-TOF
Three new prototypes were developed and tested at SPS on November of 2015. Data analysis goes smoothly.

## Slide 23
Thanks for your attention !