## Slide 1: 5D tracking concept for the next generation ATLAS muon trigger…and beyond
G. Aielli, R. Cardarelli, A. Di Ciaccio, B. Liberti, P.Camarri, L.Paolozzi, R. Santonico
Ghent– February, 24 2016

## Slide 2: Future challenges and strategies
(ATLAS was designed for LHC: L=1034 cm-2s-1 )
[Now we expect 7.5 x instantaneous and 10 x integrated luminosity]
PILEUP: from ~30>200 proton collisions/BC
Impact: High occupancy limits performance in vertex reconstruction and calorimeter. Maintain threshold for single isolated leptons as low as possible rejecting the pileup
Strategy: higher granularity and faster tracking detectors: time is a fourth coordinate  smarter Trigger DAQ

## Slide 3: To keep in mind for the future
Ultimate FCC scenario
Center of mass energy: 100 TeV
peak luminosity ultimate: ≤ 30x1034
Bunch Crossing <5 ns
integrated luminosity ultimate ~1000 fb-1 (average per year)
25 years operation, leading to ~20 ab-1
Consequence on detectors
Boosted objects up to h=6 coverage
High pileup and fast BC  very fast and granular detectors
Momentum resolution ≈15% at pT=10TeV
~1ns sharp BCID
Particle flow capability for calorimeters with high granularity 25 mrad^2
Fine timing against pileup  < 100 pS

## Slide 4: RPC event Localization and parametric space
RPC events are extremely localized occupy a tiny volume in parametric space:
E.g. one hit in 1 mm gas gap
  ~ 2 ns FWHM duration
  ~ 4 mm2 FWHM footprint
Chart: 
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0.0088388 | 0.012942 | 0.0094804 | 0.00046593 | 1.7371e-05 | 5.7736e-07 | 1.8011e-08 | 5.3969e-10 | 1.5728e-11 | 4.4909e-13 | 1.2624e-14 | 3.5054e-16 | 9.6368e-18 | 2.6275e-19 | 7.1146e-21 | 1.9151e-22 | 5.1288e-24 | 1.3674e-25
 | 0 | 0 | 0 | 0.0003125 | 0.013407 | 0.5 | 0.023509 | 0.0011984 | 5.361e-05 | 2.1411e-06 | 7.8791e-08 | 2.7323e-09 | 9.0648e-11 | 2.9066e-12 | 9.0721e-14 | 2.7706e-15 | 8.311e-17 | 2.4558e-18 | 7.1648e-20 | 2.0675e-21 | 5.9094e-23 | 1.6749e-24
 | 0 | 0 | 8.2864e-06 | 0.00047793 | 0.01665 | 0.024248 | 0.017718 | 0.0012783 | 7.2246e-05 | 3.5288e-06 | 1.5493e-07 | 6.276e-09 | 2.3894e-10 | 8.6641e-12 | 3.021e-13 | 1.0202e-14 | 3.3549e-16 | 1.0789e-17 | 3.4039e-19 | 1.0564e-20 | 3.2323e-22 | 9.7647e-24
 | 0 | 1.9531e-07 | 1.2848e-05 | 0.00044457 | 0.0012473 | 0.0017888 | 0.0013398 | 0.00053548 | 4.9072e-05 | 3.2072e-06 | 1.7527e-07 | 8.4982e-09 | 3.7736e-10 | 1.5657e-11 | 6.1549e-13 | 2.3155e-14 | 8.3993e-16 | 2.9549e-17 | 1.0128e-18 | 3.3941e-20 | 1.1154e-21 | 3.6027e-23
 | 4.3158e-09 | 3.0738e-07 | 1.0735e-05 | 4.4009e-05 | 9.3642e-05 | 0.00012079 | 0.00010069 | 5.2206e-05 | 1.5389e-05 | 1.633e-06 | 1.2105e-07 | 7.3578e-09 | 3.9197e-10 | 1.8966e-11 | 8.5209e-13 | 3.6083e-14 | 1.4557e-15 | 5.6402e-17 | 2.1118e-18 | 7.6783e-20 | 2.7216e-21 | 9.4319e-23
 | 6.8941e-09 | 2.446e-07 | 1.307e-06 | 3.6748e-06 | 6.5885e-06 | 8.1456e-06 | 7.0969e-06 | 4.3283e-06 | 1.7609e-06 | 4.3366e-07 | 5.0483e-08 | 4.1454e-09 | 2.7682e-10 | 1.6067e-11 | 8.4129e-13 | 4.0677e-14 | 1.8451e-15 | 7.9416e-17 | 3.2711e-18 | 1.2979e-19 | 4.9861e-21 | 1.8619e-22
 | 5.3609e-09 | 3.5096e-08 | 1.2235e-07 | 2.7877e-07 | 4.5209e-07 | 5.4206e-07 | 4.8757e-07 | 3.2761e-07 | 1.6091e-07 | 5.5087e-08 | 1.2103e-08 | 1.4957e-09 | 1.3331e-10 | 9.656e-12 | 6.0519e-13 | 3.4052e-14 | 1.7615e-15 | 8.5147e-17 | 3.8919e-18 | 1.697e-19 | 7.1081e-21 | 2.8741e-22
 | 8.7601e-10 | 3.6607e-09 | 1.0081e-08 | 2.0126e-08 | 3.046e-08 | 3.5765e-08 | 3.2881e-08 | 2.3631e-08 | 1.3111e-08 | 5.4758e-09 | 1.649e-09 | 3.3572e-10 | 4.3158e-11 | 4.1072e-12 | 3.1901e-13 | 2.1407e-14 | 1.2857e-15 | 7.0758e-17 | 3.6275e-18 | 1.7534e-19 | 8.0634e-21 | 3.5511e-22
Chart: 
 | 4.7639e-07 | 2.2027e-06 | 6.7032e-06 | 1.4252e-05 | 2.2286e-05 | 2.6314e-05 | 2.3709e-05 | 1.6255e-05 | 8.3532e-06 | 3.1239e-06 | 8.1709e-07 | 1.453e-07 | 1.9909e-08 | 2.2697e-09 | 2.253e-10 | 2.0042e-11 | 1.6294e-12 | 1.2278e-13 | 8.6651e-15 | 5.7747e-16 | 3.6581e-17 | 2.2447e-18
 | 2.3902e-06 | 1.7449e-05 | 6.8129e-05 | 0.00016795 | 0.00028334 | 0.00034205 | 0.00029967 | 0.00018975 | 8.4469e-05 | 2.5328e-05 | 4.8646e-06 | 7.1417e-07 | 8.722e-08 | 9.2813e-09 | 8.8529e-10 | 7.713e-11 | 6.2212e-12 | 4.6927e-13 | 3.3366e-14 | 2.2506e-15 | 1.4478e-16 | 8.9095e-18
 | 8.1795e-06 | 7.399e-05 | 0.0004486 | 0.0013831 | 0.0026239 | 0.0032639 | 0.0027524 | 0.0015433 | 0.00055454 | 0.00011608 | 1.8247e-05 | 2.371e-06 | 2.6801e-07 | 2.7156e-08 | 2.5139e-09 | 2.1547e-10 | 1.7265e-11 | 1.3032e-12 | 9.3229e-14 | 6.353e-15 | 4.1415e-16 | 2.5884e-17
 | 2.0165e-05 | 0.00020396 | 0.0015307 | 0.0075256 | 0.016918 | 0.022404 | 0.017543 | 0.0082438 | 0.0019431 | 0.00033554 | 4.722e-05 | 5.7407e-06 | 6.2318e-07 | 6.167e-08 | 5.6415e-09 | 4.8185e-10 | 3.872e-11 | 2.9459e-12 | 2.1379e-13 | 1.5091e-14 | 1.1205e-15 | 1.0701e-16
 | 3.7532e-05 | 0.00039558 | 0.0032748 | 0.019723 | 0.085362 | 0.11786 | 0.087463 | 0.021861 | 0.0042394 | 0.00066413 | 8.8879e-05 | 1.0527e-05 | 1.1295e-06 | 1.1154e-07 | 1.0251e-08 | 8.8423e-10 | 7.2293e-11 | 5.774e-12 | 5.2016e-13 | 7.6257e-14 | 1.8647e-14 | 4.7387e-15
 | 5.3977e-05 | 0.00056388 | 0.0047378 | 0.030859 | 0.15254 | 0.83254 | 0.15874 | 0.034235 | 0.0061732 | 0.00094331 | 0.00012562 | 1.4968e-05 | 1.6261e-06 | 1.6329e-07 | 1.5338e-08 | 1.3832e-09 | 1.3706e-10 | 2.3119e-11 | 7.4228e-12 | 2.6659e-12 | 8.1729e-13 | 1.9477e-13
 | 6.0636e-05 | 0.00060098 | 0.0048161 | 0.03014 | 0.14599 | 0.34942 | 0.14515 | 0.033247 | 0.0062257 | 0.00098362 | 0.00013563 | 1.6732e-05 | 1.8826e-06 | 1.9739e-07 | 2.0921e-08 | 3.3055e-09 | 1.18e-09 | 5.6322e-10 | 2.3913e-10 | 8.1795e-11 | 2.1735e-11 | 4.3164e-12
 | 5.3226e-05 | 0.00048031 | 0.0034423 | 0.018693 | 0.063929 | 0.08703 | 0.065369 | 0.020328 | 0.0043625 | 0.00075754 | 0.00011253 | 1.4824e-05 | 1.814e-06 | 2.5684e-07 | 8.0122e-08 | 4.7942e-08 | 2.848e-08 | 1.3901e-08 | 5.3369e-09 | 1.5652e-09 | 3.4113e-10 | 5.4411e-11
 | 3.6232e-05 | 0.00028431 | 0.0016981 | 0.006892 | 0.014666 | 0.019085 | 0.015218 | 0.0075451 | 0.0020959 | 0.00042764 | 7.1909e-05 | 1.1144e-05 | 2.5434e-06 | 1.567e-06 | 1.3152e-06 | 9.4654e-07 | 5.3907e-07 | 2.3665e-07 | 7.785e-08 | 1.8594e-08 | 3.187e-09 | 4.2472e-10
 | 1.8817e-05 | 0.0001218 | 0.00055329 | 0.0015214 | 0.0027413 | 0.0033609 | 0.0028688 | 0.0016856 | 0.00066958 | 0.00017567 | 4.0228e-05 | 1.7939e-05 | 1.9942e-05 | 2.266e-05 | 2.0343e-05 | 1.3973e-05 | 7.217e-06 | 2.725e-06 | 7.2543e-07 | 1.3315e-07 | 1.8944e-08 | 2.2297e-09
 | 7.2873e-06 | 3.6635e-05 | 0.00011963 | 0.00026941 | 0.00043507 | 0.00051756 | 0.00045802 | 0.00030116 | 0.00014675 | 6.4307e-05 | 6.7127e-05 | 0.00013611 | 0.00022492 | 0.00027059 | 0.00023709 | 0.00015052 | 6.7433e-05 | 2.0486e-05 | 4.0421e-06 | 6.1294e-07 | 7.7226e-08 | 8.4023e-09
 | 2.0572e-06 | 7.8316e-06 | 2.0822e-05 | 4.1061e-05 | 6.172e-05 | 7.1854e-05 | 6.5289e-05 | 4.6778e-05 | 3.2112e-05 | 6.8233e-05 | 0.00034954 | 0.0010673 | 0.0020243 | 0.0025177 | 0.0021221 | 0.0011884 | 0.00042652 | 8.95e-05 | 1.4474e-05 | 1.9523e-06 | 2.2887e-07 | 2.382e-08
Chart: 
 | 1.1187e-05 | 3.6714e-05 | 9.3501e-05 | 0.00017953 | 0.00026541 | 0.00030615 | 0.00027717 | 0.00019676 | 0.0001088 | 4.6364e-05 | 1.5115e-05 | 3.8089e-06 | 7.8123e-07 | 1.361e-07 | 2.0775e-08 | 2.8426e-09 | 3.5456e-10 | 4.0838e-11 | 4.3875e-12 | 4.4363e-13 | 4.2697e-14 | 4.133e-15
 | 3.9788e-05 | 0.00016847 | 0.00049523 | 0.0010495 | 0.0016392 | 0.0019206 | 0.0017 | 0.0011358 | 0.00056756 | 0.0002107 | 5.8701e-05 | 1.3182e-05 | 2.5007e-06 | 4.1385e-07 | 6.1139e-08 | 8.2019e-09 | 1.0124e-09 | 1.162e-10 | 1.253e-11 | 1.2906e-12 | 1.3329e-13 | 1.5462e-14
 | 0.00011043 | 0.00053878 | 0.0019402 | 0.0047475 | 0.0080642 | 0.0096676 | 0.008293 | 0.0050599 | 0.0021863 | 0.00067076 | 0.00016351 | 3.3451e-05 | 5.9461e-06 | 9.4058e-07 | 1.3474e-07 | 1.7715e-08 | 2.1619e-09 | 2.48e-10 | 2.752e-11 | 3.253e-12 | 5.1295e-13 | 1.1456e-13
 | 0.00023335 | 0.0012508 | 0.0052105 | 0.016152 | 0.031035 | 0.038889 | 0.031563 | 0.016877 | 0.0057803 | 0.001549 | 0.00034539 | 6.6543e-05 | 1.1354e-05 | 1.7468e-06 | 2.4576e-07 | 3.2014e-08 | 3.9298e-09 | 4.7904e-10 | 6.9073e-11 | 1.5409e-11 | 4.8799e-12 | 1.5194e-12
 | 0.00038404 | 0.0021612 | 0.0097652 | 0.034529 | 0.088664 | 0.11508 | 0.088641 | 0.035072 | 0.010674 | 0.0026562 | 0.00056549 | 0.00010578 | 1.7724e-05 | 2.7004e-06 | 3.7954e-07 | 5.0533e-08 | 7.0043e-09 | 1.3281e-09 | 4.1871e-10 | 1.648e-10 | 6.1307e-11 | 1.8748e-11
 | 0.00049956 | 0.0028356 | 0.013073 | 0.048146 | 0.1316 | 0.24757 | 0.12652 | 0.048152 | 0.014122 | 0.0034522 | 0.00072861 | 0.00013602 | 2.2867e-05 | 3.5263e-06 | 5.2012e-07 | 8.6171e-08 | 2.2838e-08 | 9.7443e-09 | 4.5295e-09 | 1.8774e-09 | 6.5567e-10 | 1.8295e-10
 | 0.00051786 | 0.0028569 | 0.012735 | 0.04473 | 0.11481 | 0.1664 | 0.11227 | 0.044624 | 0.013672 | 0.0034452 | 0.00074604 | 0.00014271 | 2.4772e-05 | 4.1763e-06 | 8.8154e-07 | 3.3665e-07 | 1.8527e-07 | 9.9747e-08 | 4.6059e-08 | 1.7635e-08 | 5.5242e-09 | 1.372e-09
 | 0.00042888 | 0.0022201 | 0.0090896 | 0.028366 | 0.059691 | 0.07519 | 0.059632 | 0.028735 | 0.009799 | 0.0027099 | 0.00067861 | 0.00018078 | 5.3955e-05 | 1.5483e-05 | 4.7416e-06 | 2.8206e-06 | 1.7362e-06 | 9.0209e-07 | 3.8238e-07 | 1.3068e-07 | 3.588e-08 | 7.8299e-09
 | 0.0002833 | 0.0013298 | 0.0047769 | 0.012493 | 0.022096 | 0.026849 | 0.022387 | 0.01297 | 0.006082 | 0.0040855 | 0.0039864 | 0.0027854 | 0.0011167 | 0.00013487 | 3.8155e-05 | 2.3723e-05 | 1.398e-05 | 6.6637e-06 | 2.5132e-06 | 7.463e-07 | 1.769e-07 | 3.4263e-08
 | 0.00014865 | 0.00061392 | 0.001871 | 0.004128 | 0.0066262 | 0.0077991 | 0.0067855 | 0.0044543 | 0.0046917 | 0.047921 | 0.068573 | 0.050032 | 0.0049213 | 0.00061397 | 0.00025893 | 0.00016874 | 9.2311e-05 | 3.9109e-05 | 1.2688e-05 | 3.1985e-06 | 6.6518e-07 | 1.1699e-07
 | 6.18e-05 | 0.00022041 | 0.000572 | 0.0011216 | 0.0016794 | 0.0019387 | 0.0017389 | 0.0014039 | 0.0056613 | 0.070617 | 0.5 | 0.072044 | 0.0092363 | 0.0023168 | 0.0015336 | 0.00098922 | 0.00048439 | 0.00017483 | 4.7002e-05 | 1.0312e-05 | 1.9401e-06 | 3.1783e-07
 | 2.0486e-05 | 6.3578e-05 | 0.00014584 | 0.00026192 | 0.00037302 | 0.00042482 | 0.00039841 | 0.00056683 | 0.0050358 | 0.051199 | 0.074455 | 0.057313 | 0.014124 | 0.0095985 | 0.0076911 | 0.0045753 | 0.0019039 | 0.0005502 | 0.00012804 | 2.5459e-05 | 4.4729e-06 | 6.9885e-07
Chart: 
 | 1.8316e-05 | 5.6508e-05 | 0.0001388 | 0.00026067 | 0.00038057 | 0.00043672 | 0.00039592 | 0.0002834 | 0.00015934 | 6.9844e-05 | 2.379e-05 | 6.3795e-06 | 1.4077e-06 | 2.6531e-07 | 4.3934e-08 | 6.5271e-09 | 8.8399e-10 | 1.105e-10 | 1.2878e-11 | 1.4135e-12 | 1.486e-13 | 1.611e-14
 | 6.1059e-05 | 0.0002394 | 0.00066824 | 0.0013732 | 0.0021094 | 0.0024558 | 0.0021794 | 0.0014738 | 0.00075486 | 0.0002922 | 8.6738e-05 | 2.0979e-05 | 4.3102e-06 | 7.745e-07 | 1.2434e-07 | 1.8125e-08 | 2.4295e-09 | 3.027e-10 | 3.5475e-11 | 4.0072e-12 | 4.6934e-13 | 6.529e-14
 | 0.00016274 | 0.00072429 | 0.0024051 | 0.0056193 | 0.0093163 | 0.011075 | 0.0095408 | 0.0059344 | 0.0026656 | 0.00087418 | 0.00023003 | 5.1038e-05 | 9.8611e-06 | 1.6967e-06 | 2.6434e-07 | 3.7775e-08 | 5.0091e-09 | 6.2594e-10 | 7.6742e-11 | 1.0474e-11 | 1.9909e-12 | 5.0496e-13
 | 0.00033418 | 0.001621 | 0.0061277 | 0.017405 | 0.032147 | 0.0397 | 0.032537 | 0.017993 | 0.0066519 | 0.0019345 | 0.00046905 | 9.8346e-05 | 1.8266e-05 | 3.058e-06 | 4.6791e-07 | 6.6295e-08 | 8.8903e-09 | 1.2087e-09 | 2.0336e-10 | 5.2643e-11 | 1.7932e-11 | 5.7603e-12
 | 0.00053841 | 0.0027326 | 0.011114 | 0.035403 | 0.08195 | 0.1044 | 0.081504 | 0.035519 | 0.011852 | 0.0032247 | 0.00074912 | 0.00015273 | 2.7863e-05 | 4.6189e-06 | 7.0674e-07 | 1.0315e-07 | 1.6094e-08 | 3.5362e-09 | 1.2278e-09 | 5.0189e-10 | 1.9127e-10 | 5.989e-11
 | 0.00068936 | 0.0035267 | 0.014598 | 0.04814 | 0.11759 | 0.19546 | 0.113 | 0.047585 | 0.015375 | 0.0041192 | 0.00094976 | 0.00019339 | 3.5485e-05 | 6.0026e-06 | 9.8475e-07 | 1.8521e-07 | 5.4656e-08 | 2.4422e-08 | 1.1575e-08 | 4.891e-09 | 1.7522e-09 | 5.0409e-10
 | 0.0007067 | 0.0035199 | 0.014106 | 0.044527 | 0.10292 | 0.14123 | 0.10049 | 0.043977 | 0.0148 | 0.0040924 | 0.00098014 | 0.00021503 | 4.6692e-05 | 1.0609e-05 | 2.5613e-06 | 8.0687e-07 | 4.0701e-07 | 2.1796e-07 | 1.0206e-07 | 3.999e-08 | 1.2943e-08 | 3.3475e-09
 | 0.00058177 | 0.0027306 | 0.010113 | 0.028709 | 0.056357 | 0.06977 | 0.056105 | 0.028883 | 0.010859 | 0.0035757 | 0.0013297 | 0.00062676 | 0.00027622 | 8.5025e-05 | 1.642e-05 | 5.9981e-06 | 3.3348e-06 | 1.7314e-06 | 7.4796e-07 | 2.6346e-07 | 7.5485e-08 | 1.7356e-08
 | 0.00038444 | 0.0016493 | 0.0054256 | 0.013229 | 0.022555 | 0.02704 | 0.02277 | 0.013799 | 0.0083096 | 0.0084872 | 0.009727 | 0.0071239 | 0.0029916 | 0.00045567 | 9.1273e-05 | 4.1953e-05 | 2.3659e-05 | 1.14e-05 | 4.4162e-06 | 1.3659e-06 | 3.4218e-07 | 7.0488e-08
 | 0.00020358 | 0.00077832 | 0.0022163 | 0.0046803 | 0.0073301 | 0.0085521 | 0.007501 | 0.005435 | 0.0092568 | 0.05491 | 0.077183 | 0.056322 | 0.008973 | 0.0013968 | 0.0004431 | 0.0002559 | 0.00013933 | 6.0381e-05 | 2.0374e-05 | 5.4343e-06 | 1.2065e-06 | 2.2706e-07
 | 8.6448e-05 | 0.00029062 | 0.00072027 | 0.0013704 | 0.002017 | 0.0023145 | 0.002122 | 0.0023059 | 0.011286 | 0.078807 | 1 | 0.092902 | 0.015027 | 0.0037314 | 0.0021008 | 0.0013193 | 0.00065735 | 0.00024671 | 7.0509e-05 | 1.6567e-05 | 3.3489e-06 | 5.8902e-07
 | 2.9706e-05 | 8.8567e-05 | 0.0001967 | 0.00034567 | 0.00048614 | 0.00055328 | 0.00056491 | 0.0012743 | 0.0091151 | 0.06652 | 0.095536 | 0.073413 | 0.01955 | 0.011781 | 0.0090139 | 0.0054203 | 0.0023452 | 0.00072801 | 0.00018279 | 3.9212e-05 | 7.4284e-06 | 1.2482e-06
Chart: 
 | 4.775e-05 | 0.00012931 | 0.00029304 | 0.00052291 | 0.00074126 | 0.00084034 | 0.00076453 | 0.00055828 | 0.00032656 | 0.00015271 | 5.7286e-05 | 1.751e-05 | 4.5013e-06 | 1.0011e-06 | 1.9699e-07 | 3.49e-08 | 5.6445e-09 | 8.4288e-10 | 1.1747e-10 | 1.5515e-11 | 2.0118e-12 | 2.8764e-13
 | 0.00013842 | 0.00046603 | 0.0011618 | 0.002223 | 0.0032818 | 0.0037622 | 0.0033605 | 0.0023412 | 0.0012714 | 0.00054103 | 0.00018381 | 5.1973e-05 | 1.2628e-05 | 2.7004e-06 | 5.1755e-07 | 9.0176e-08 | 1.4453e-08 | 2.1558e-09 | 3.0474e-10 | 4.2741e-11 | 6.6795e-12 | 1.2934e-12
 | 0.00033666 | 0.0012458 | 0.0034975 | 0.0073536 | 0.011503 | 0.013394 | 0.011668 | 0.007609 | 0.0037422 | 0.0014169 | 0.00043902 | 0.00011577 | 2.671e-05 | 5.4999e-06 | 1.0262e-06 | 1.7573e-07 | 2.7985e-08 | 4.245e-09 | 6.5537e-10 | 1.2073e-10 | 3.0824e-11 | 9.1659e-12
 | 0.00064713 | 0.0025603 | 0.0079007 | 0.01877 | 0.031657 | 0.037798 | 0.031721 | 0.018993 | 0.0082408 | 0.0028555 | 0.00082916 | 0.00020857 | 4.651e-05 | 9.3569e-06 | 1.7244e-06 | 2.9621e-07 | 4.9007e-08 | 8.5517e-09 | 1.9113e-09 | 6.0821e-10 | 2.2785e-10 | 7.7043e-11
 | 0.00099371 | 0.0040758 | 0.013291 | 0.034173 | 0.065087 | 0.079396 | 0.064175 | 0.033648 | 0.013585 | 0.0044754 | 0.0012565 | 0.00030954 | 6.8561e-05 | 1.4004e-05 | 2.7184e-06 | 5.2135e-07 | 1.0728e-07 | 2.8471e-08 | 1.0619e-08 | 4.4977e-09 | 1.7891e-09 | 5.8846e-10
 | 0.0012297 | 0.0050734 | 0.016751 | 0.044088 | 0.086944 | 0.11861 | 0.083842 | 0.042869 | 0.016933 | 0.0055328 | 0.0015634 | 0.0004007 | 9.9234e-05 | 2.5165e-05 | 6.4778e-06 | 1.6237e-06 | 4.4422e-07 | 1.6785e-07 | 7.5756e-08 | 3.2707e-08 | 1.2341e-08 | 3.7864e-09
 | 0.0012339 | 0.0049768 | 0.015988 | 0.040691 | 0.077277 | 0.096787 | 0.075342 | 0.039681 | 0.016298 | 0.0056692 | 0.0018805 | 0.00068794 | 0.00027976 | 0.00010543 | 3.1572e-05 | 7.8361e-06 | 2.4978e-06 | 1.0977e-06 | 5.0354e-07 | 2.0545e-07 | 7.1278e-08 | 2.0062e-08
 | 0.0010077 | 0.003871 | 0.011675 | 0.027487 | 0.047286 | 0.056373 | 0.046849 | 0.02765 | 0.013291 | 0.0068851 | 0.0046035 | 0.0031554 | 0.0016667 | 0.00059789 | 0.00013945 | 3.5648e-05 | 1.3766e-05 | 6.5077e-06 | 2.867e-06 | 1.0754e-06 | 3.3779e-07 | 8.6559e-08
 | 0.0006713 | 0.0024011 | 0.0066142 | 0.014026 | 0.022117 | 0.025786 | 0.022336 | 0.015625 | 0.014721 | 0.020757 | 0.025088 | 0.01913 | 0.0088364 | 0.0020522 | 0.00045827 | 0.00014839 | 6.9607e-05 | 3.3154e-05 | 1.3548e-05 | 4.5862e-06 | 1.2948e-06 | 3.0352e-07
 | 0.00036576 | 0.0011986 | 0.0029728 | 0.005715 | 0.0084792 | 0.0097296 | 0.0089348 | 0.008841 | 0.021735 | 0.088539 | 0.12126 | 0.089546 | 0.021183 | 0.0046426 | 0.0013135 | 0.00059794 | 0.00030972 | 0.00013997 | 5.1639e-05 | 1.5615e-05 | 3.9999e-06 | 8.6957e-07
 | 0.00016395 | 0.00048939 | 0.0010989 | 0.0019548 | 0.0027698 | 0.0031725 | 0.0033159 | 0.0060234 | 0.026847 | 0.12278 | 0.47211 | 0.11981 | 0.030842 | 0.0085666 | 0.0038856 | 0.0022366 | 0.0011468 | 0.00047056 | 0.00015417 | 4.2229e-05 | 1.0009e-05 | 2.0534e-06
 | 6.1208e-05 | 0.00016773 | 0.00034669 | 0.0005799 | 0.00079574 | 0.000939 | 0.0013127 | 0.0042996 | 0.021331 | 0.087782 | 0.1219 | 0.094662 | 0.032946 | 0.017029 | 0.011585 | 0.0070508 | 0.0033294 | 0.0012061 | 0.00035856 | 9.1254e-05 | 2.0469e-05 | 4.0346e-06
Chart: 
 | 0.00015284 | 0.00034005 | 0.00067513 | 0.0011013 | 0.0014798 | 0.0016411 | 0.0015045 | 0.0011415 | 0.00071796 | 0.00037567 | 0.00016482 | 6.1467e-05 | 1.9852e-05 | 5.6538e-06 | 1.4424e-06 | 3.3421e-07 | 7.1187e-08 | 1.4112e-08 | 2.645e-09 | 4.821e-10 | 9.0535e-11 | 1.9682e-11
 | 0.0003571 | 0.00098005 | 0.0020519 | 0.0034804 | 0.0047865 | 0.0053381 | 0.0048326 | 0.0035597 | 0.0021431 | 0.0010645 | 0.00044332 | 0.00015829 | 4.9452e-05 | 1.3758e-05 | 3.4616e-06 | 7.99e-07 | 1.7169e-07 | 3.4955e-08 | 6.937e-09 | 1.4206e-09 | 3.2887e-10 | 8.5131e-11
 | 0.00074662 | 0.0021593 | 0.0047968 | 0.016932 | 0.0244 | 0.022614 | 0.012571 | 0.0086128 | 0.0049026 | 0.002293 | 0.00090601 | 0.00031008 | 9.3932e-05 | 2.5679e-05 | 6.4597e-06 | 1.5263e-06 | 3.4623e-07 | 7.7393e-08 | 1.7866e-08 | 4.6295e-09 | 1.4231e-09 | 4.5234e-10
 | 0.0012836 | 0.0038537 | 0.0092849 | 0.029583 | 0.5 | 0.050416 | 0.025664 | 0.01671 | 0.0089908 | 0.0040108 | 0.0015277 | 0.00051097 | 0.00015428 | 4.3365e-05 | 1.1718e-05 | 3.115e-06 | 8.2051e-07 | 2.1726e-07 | 6.1476e-08 | 2.005e-08 | 7.3309e-09 | 2.5071e-09
 | 0.001822 | 0.0055927 | 0.013869 | 0.041889 | 0.062779 | 0.062294 | 0.040195 | 0.025413 | 0.013229 | 0.0057695 | 0.0021888 | 0.00075422 | 0.00024875 | 8.2188e-05 | 2.7316e-05 | 0.0088475 | 0.012944 | 0.0094811 | 0.00046618 | 1.7468e-05 | 6.1492e-07 | 3.0866e-08
 | 0.0021444 | 0.0066028 | 0.016347 | 0.03244 | 0.049917 | 0.057409 | 0.047446 | 0.030294 | 0.015786 | 0.0070735 | 0.002926 | 0.0012168 | 0.00053056 | 0.00023027 | 0.00040336 | 0.013438 | 0.5 | 0.023512 | 0.0011995 | 5.4059e-05 | 2.3162e-06 | 1.3691e-07
 | 0.0021013 | 0.006373 | 0.015151 | 0.029211 | 0.044321 | 0.050771 | 0.043416 | 0.028772 | 0.016082 | 0.0085211 | 0.004843 | 0.0029511 | 0.0016959 | 0.00082735 | 0.0007964 | 0.016753 | 0.02428 | 0.017729 | 0.001283 | 7.4142e-05 | 4.2452e-06 | 3.8192e-07
 | 0.0017216 | 0.0050586 | 0.011572 | 0.021437 | 0.031371 | 0.035574 | 0.031505 | 0.023139 | 0.016591 | 0.013781 | 0.01225 | 0.0095279 | 0.0057514 | 0.0026192 | 0.0013586 | 0.0015406 | 0.0018906 | 0.0013807 | 0.0005529 | 5.6092e-05 | 5.7313e-06 | 9.3278e-07
 | 0.001185 | 0.0033374 | 0.0072525 | 0.01277 | 0.018033 | 0.020416 | 0.019261 | 0.017928 | 0.021988 | 0.03039 | 0.034541 | 0.027811 | 0.015586 | 0.0061389 | 0.0021315 | 0.00082635 | 0.00041954 | 0.00023428 | 0.00010985 | 3.7692e-05 | 9.1939e-06 | 2.27e-06
 | 0.00068992 | 0.0018493 | 0.0037959 | 0.0063617 | 0.0087422 | 0.010069 | 0.010907 | 0.015231 | 0.030944 | 0.061804 | 0.076441 | 0.060127 | 0.028169 | 0.010865 | 0.0040675 | 0.0017389 | 0.00083639 | 0.00039572 | 0.00016766 | 6.1577e-05 | 1.957e-05 | 5.2309e-06
 | 0.00034275 | 0.00087351 | 0.0016977 | 0.0027286 | 0.0037004 | 0.0045271 | 0.0063213 | 0.013391 | 0.034825 | 0.076189 | 0.11804 | 0.074291 | 0.036475 | 0.015827 | 0.0074852 | 0.0039677 | 0.0020769 | 0.00096723 | 0.00038753 | 0.00013445 | 4.0935e-05 | 1.0652e-05
 | 0.00014707 | 0.00035795 | 0.00066349 | 0.0010341 | 0.0014204 | 0.0019883 | 0.0038279 | 0.010393 | 0.028021 | 0.058654 | 0.074776 | 0.063281 | 0.037211 | 0.021835 | 0.013722 | 0.0083594 | 0.0044433 | 0.0019893 | 0.0007593 | 0.00025193 | 7.3896e-05 | 1.8696e-05
Chart: 
 | 0.0001909 | 0.00041479 | 0.00081865 | 0.0013265 | 0.0017536 | 0.0019024 | 0.0017099 | 0.0012882 | 0.00081871 | 0.0004406 | 0.00020108 | 7.8733e-05 | 2.6878e-05 | 8.1311e-06 | 2.212e-06 | 5.4848e-07 | 1.2556e-07 | 2.6904e-08 | 5.492e-09 | 1.1003e-09 | 2.2828e-10 | 5.4234e-11
 | 0.00042429 | 0.0011545 | 0.0030306 | 0.0058447 | 0.008038 | 0.0078081 | 0.0059332 | 0.0038337 | 0.0023137 | 0.0011904 | 0.00052033 | 0.00019648 | 6.5305e-05 | 1.9666e-05 | 6.0472e-06 | 2.7839e-06 | 2.1446e-06 | 1.6699e-06 | 9.8514e-07 | 3.9114e-07 | 9.2325e-08 | 9.3681e-09
 | 0.00085541 | 0.0024633 | 0.0071989 | 0.045607 | 0.065411 | 0.052247 | 0.015537 | 0.0087745 | 0.0050151 | 0.0024531 | 0.001026 | 0.00037409 | 0.00012169 | 4.6515e-05 | 5.3801e-05 | 9.6187e-05 | 0.00012143 | 0.00010085 | 5.2246e-05 | 1.54e-05 | 1.6365e-06 | 1.2198e-07
 | 0.0014311 | 0.0042472 | 0.013013 | 0.070977 | 1 | 0.095763 | 0.0289 | 0.016089 | 0.0088232 | 0.0041538 | 0.0016882 | 0.00060742 | 0.00020085 | 0.00010859 | 0.00086196 | 0.0022963 | 0.0032489 | 0.0024464 | 0.00099882 | 0.00011191 | 9.1036e-06 | 6.1785e-07
 | 0.0019918 | 0.005967 | 0.016769 | 0.073796 | 0.10675 | 0.091627 | 0.039691 | 0.023425 | 0.012651 | 0.0058779 | 0.0024083 | 0.00091018 | 0.00033907 | 0.0002585 | 0.0024379 | 0.02979 | 0.042867 | 0.03127 | 0.0035878 | 0.00033196 | 2.5722e-05 | 1.7541e-06
 | 0.0023147 | 0.006843 | 0.017258 | 0.033598 | 0.049078 | 0.052813 | 0.042515 | 0.027285 | 0.015004 | 0.0072681 | 0.0033178 | 0.0015391 | 0.00074823 | 0.00057864 | 0.0042118 | 0.043988 | 1 | 0.061949 | 0.0061171 | 0.0005541 | 4.4489e-05 | 3.2396e-06
 | 0.0022548 | 0.0064923 | 0.014573 | 0.026594 | 0.038592 | 0.043355 | 0.037571 | 0.026032 | 0.015626 | 0.0091009 | 0.0056622 | 0.003665 | 0.0022084 | 0.0013823 | 0.0041147 | 0.044317 | 0.063536 | 0.046387 | 0.0054264 | 0.00056171 | 5.0901e-05 | 4.2695e-06
 | 0.0018508 | 0.0051443 | 0.011098 | 0.019557 | 0.027696 | 0.031111 | 0.02807 | 0.021734 | 0.016807 | 0.014714 | 0.013314 | 0.0105 | 0.0065585 | 0.0033475 | 0.0032657 | 0.0057343 | 0.0075534 | 0.0056852 | 0.0024011 | 0.00035105 | 4.0963e-05 | 4.576e-06
 | 0.0012873 | 0.0034484 | 0.0071213 | 0.012046 | 0.016615 | 0.018769 | 0.018221 | 0.017912 | 0.022075 | 0.029419 | 0.032707 | 0.026708 | 0.015775 | 0.0069667 | 0.002906 | 0.0016002 | 0.0011984 | 0.00084602 | 0.00043604 | 0.00014675 | 2.8866e-05 | 5.2954e-06
 | 0.00076425 | 0.001964 | 0.0038669 | 0.0062841 | 0.0085078 | 0.0098924 | 0.011186 | 0.015949 | 0.029833 | 0.053011 | 0.0637 | 0.051265 | 0.026965 | 0.011679 | 0.0048036 | 0.0021655 | 0.0010866 | 0.00054745 | 0.00025026 | 9.7689e-05 | 3.1742e-05 | 8.3809e-06
 | 0.00039052 | 0.00096219 | 0.0018099 | 0.0028451 | 0.0038424 | 0.0048282 | 0.0070284 | 0.014267 | 0.032831 | 0.063392 | 0.087906 | 0.062368 | 0.034271 | 0.016493 | 0.0082536 | 0.0044733 | 0.0023991 | 0.0011549 | 0.00047926 | 0.00017243 | 5.5441e-05 | 1.5217e-05
 | 0.00017371 | 0.00041196 | 0.00074532 | 0.0011471 | 0.001593 | 0.0023242 | 0.0045075 | 0.011202 | 0.026761 | 0.050322 | 0.062748 | 0.054564 | 0.035167 | 0.022454 | 0.015893 | 0.011495 | 0.0069109 | 0.0030954 | 0.00097111 | 0.00031392 | 9.6136e-05 | 2.5704e-05
Ds=10 mm2
Dt=2ns
The equivalent parametric space of 1 cm2 x 1 s can contain ~ 5 x 109 separable states
1 GHz/cm2 would produce ~10% occupancy
t(ns)
0
1
2
3
4
5
6

## Slide 5: The timing features of rpcs
Signal fluctuations --> affect just the Absolute resolution
  Ionization and multiplication fluctuations are irreducible
  large dynamic range of the avalanche  can be compensated
Signal raise time  depends on the gap width
  A short rise time compresses the signal fluctuations
Affecting absolute and relative resolution
Electronics peaking time  in the ideal integrator is 0
  Should be << than the signal rise time to preserve timing information
Electronic noise 
  Overlaps to the signal and smears the discrimination time
Digitization binning
  Better if small with respect to the expected absolute resolution
Signal propagation (for strip lines)
  Can be eliminated by determining T0
Absolute resolution  fluctuations w.r.t. an external coherent source
Relative resolution  fluctuations of multiple pickup of the same external signal (2D, CS..)
Time (ns)
Time (ns)
Time (ns)
Amplitude (mV)
Amplitude (mV)
Amplitude (mV)
Duration about 3 nsec
Duration about 1.7 nsec
Duration about 1.0 nsec

## Slide 6: The tracking features of rpcs
Planar detector with homogeneous 2D planar resolution
  The intrinsic space resolution is given by the localization of the avalanche. Results better than 50 m have been reported. With a standard gas gap of 1mm 100  m have been reached with the centroid method
  The induced prompt charge distribution  depends on  which is the avalanche footprint on the readout electrodes. In the example =1.08 mm
Chart: Charge distribution binned in 1D projection
Integral charge per strip | 0.025038 | 0.040769 | 0.066353 | 0.10786 | 0.17479 | 0.28091 | 0.442 | 0.6609 | 0.88657 | 0.99023 | 0.88657 | 0.6609 | 0.442 | 0.28091 | 0.17479 | 0.10786 | 0.066353 | 0.040769 | 0.025038 | 0.015374
2
  The RPC has a linear response in terms of simultaneous track density better than 1 hit/mm2
  The ability of distinguishing neighboring hits the hits is limited primarily by 
  Simultaneous multiple tracks can be separated at a distance ~ providing an appropriate segmentation of the readout electrodes
1.2 mm
1.2 mm
1 mm

## Slide 7: Trak to track separation problem (pad vs strips)
2N readout channels to localize the hit in 2D
FE away from the sensitive area
Ambiguity in case of multiple simultaneous hits
No ambiguity on multiple tracks down to the PAD pitch
N2 readout channels to localize the hit in 2D
FE localized on sensitive area and complex cabling

## Slide 8: Trak to track separation problem (1D meantimer)
1D meantimer readout disadvantages
  Asymmetric resolution on the second coordinate
  2 amplifiers on the same strip  difficult layout for fast signals
  Large uncertainty for >1 hits on the same strip. However the probability of ambiguous events is reduced by 1/N (N= number of strips)
1D meantimer readout
Use the timing the signal pick up at both ends of the strips to determine the second coordinate (t1-t2) and T0 (t1+t2)/2
  Intrinsically robust against ghosts in multiple tracks
  The uncertainty is driven by the digitization binning (e.g. 200ps  3/ cm)
x1
X2
L = x1+x2 = V(t1+t2-2t0)
t0 = 1/2[(t1+t2)-L/v]
(x1;t1)
(x2;t2)
L
doi:10.1016/j.nima.2013.02.044

## Slide 9: Trak to track separation problem (1D meantimer)
1D meantimer readout disadvantages
  Asymmetric resolution on the second coordinate
  2 amplifiers on the same strip  difficult layout for fast signals
  Large uncertainty for >1 hits on the same strip. However the probability of ambiguous events is reduced by 1/N (N= number of strips)
1D meantimer readout
Use the timing the signal pick up at both ends of the strips to determine the second coordinate (t1-t2) and T0 (t1+t2)/2
  Intrinsically robust against ghosts in multiple tracks
  The uncertainty is driven by the digitization binning (e.g. 200ps  3/ cm)
x1
X2
L = x1+x2 = V(t1+t2-2t0)
t0 = 1/2[(t1+t2)-L/v]
(x1;t1)
(x2;t2)
L

## Slide 10: The 2d meantimer concept
Combining the advantages of x-y strip readout and of the meantimer.
2N channels for 2D homogeneous readout
No limitation of the detector resolution due to the meantimer
Electronics out of the active area
Performance driven by the FE electronics and the digitization: it requires high performance Amplifier-discriminator-TDC chain
Conceptually it is compatible with the classic ATLAS RPC layout down to the discriminator so it can be retrofitted on the present ATLAS RPCs. It would be sufficient to replace the readout electronics

## Slide 11: 2D meantimer basic definitions
d >> d  CSz1  dy20-30 mm
Classic ATLAS case, spatial resolution limited by the strip pitch
(yl;tyl;qylclus)
(yk;tyk;qykclus)
(xi;txi;qxiclus)
(xj;txj;qxjclus)
Definitions
t0= real impact time
v= signal propagation velocity (~0.15 m/ns)
2d= avalanche signal distribution width (FWHM)
d= strip pitch
tn= lowest time of a given cluster
xn= strip id with the lowest time of a given cluster
yn= strip id with the lowest time of a given cluster
qylclus=qylestimated charge of the cluster (through ToT)
Cluster list:
yl; yk;
xi; xj;
Real hit list:
a (xi; yl)
b (xj; yk)
Fake hit list:
g (xi; yk)
d (xj; yl)
g
d
Chart: 
Integral charge per strip | 0.025038 | 0.040769 | 0.066353 | 0.10786 | 0.17479 | 0.28091 | 0.442 | 0.6609 | 0.88657 | 0.99023 | 0.88657 | 0.6609 | 0.442 | 0.28091 | 0.17479 | 0.10786 | 0.066353 | 0.040769 | 0.025038 | 0.015374
b
Chart: 
Integral charge per strip | 0.025038 | 0.040769 | 0.066353 | 0.10786 | 0.17479 | 0.28091 | 0.442 | 0.6609 | 0.88657 | 0.99023 | 0.88657 | 0.6609 | 0.442 | 0.28091 | 0.17479 | 0.10786 | 0.066353 | 0.040769 | 0.025038 | 0.015374
a
Pitch and CS
d < yd  CSz3  dy1-2 mm
Best configuration for maximum resolution
Chart: 
Integral charge per strip | 0.025038 | 0.040769 | 0.066353 | 0.10786 | 0.17479 | 0.28091 | 0.442 | 0.6609 | 0.88657 | 0.99023 | 0.88657 | 0.6609 | 0.442 | 0.28091 | 0.17479 | 0.10786 | 0.066353 | 0.040769 | 0.025038 | 0.015374
2d

## Slide 12: 2D meantimer properties
(yl;tyl;qylclus)
(yk;tyk;qykclus)
(xi;txi;qxiclus)
(xj;txj;qxjclus)
Cluster list:
yl; yk;
xi; xj;
Real hit list:
a (xi; yl)
b (xj; yk)
Fake hit list:
g (xi; yk)
d (xj; yl)
g
d
Chart: 
Integral charge per strip | 0.025038 | 0.040769 | 0.066353 | 0.10786 | 0.17479 | 0.28091 | 0.442 | 0.6609 | 0.88657 | 0.99023 | 0.88657 | 0.6609 | 0.442 | 0.28091 | 0.17479 | 0.10786 | 0.066353 | 0.040769 | 0.025038 | 0.015374
b
Chart: 
Integral charge per strip | 0.025038 | 0.040769 | 0.066353 | 0.10786 | 0.17479 | 0.28091 | 0.442 | 0.6609 | 0.88657 | 0.99023 | 0.88657 | 0.6609 | 0.442 | 0.28091 | 0.17479 | 0.10786 | 0.066353 | 0.040769 | 0.025038 | 0.015374
a
Properties of real hits


## Slide 13: Preliminary results of 2015 test beam
Preliminary test on the ATLAS BIS78 prototype
2D readout connected to a CAEN digitizer DT5742
2.5 G samples/s (non optimal  0.4 ns binning. 5 G samples/s not compatible with the trigger window)
12 m lemo cables  a few cm of length difference
Anyway we did the exercise….
2D readout
1 mm gas gap
1.2 mm electrodes
100 x 50 cm^2 single gap
25 mm pitch strips
New Front end

## Slide 14: 2D meantimer observables
Determination of the real hits a, b...
Given a list of x anf y hits we can calculate the
The resulting matrix will have elements compatible with corresponding to the strips .
Calibration
The distribution of ni1, or t0i1 (for single hits) gives the the measure of v/d and uncertainty distribution calibration. It’s a property of the system
Uncertainty
TDC bin; cable length, amplifier saturation, charge dispersion, strip pitch… FE noise contribution negligible
15.9 cm/ns
For a given
15.85 cm/ns

## Slide 15: 2D meantimer Dt-Dxy test
Calibration matrix
Using a sufficient statistics of single hits one can refine the calibration by measuring a calibration and error matrix:
Respectively the local distribution of and its variance
Compatibility with a real hit
62% fake cut
Calibration curve with single hits
Fake hits distribution
The peak is displaced by taking wrongly coupled hits,
the width is broadened by taking different avalanches

## Slide 16: The fifth dimension ?
Use of the charge for close tracks disambiguation:
The time based method can certainly disambiguate track which are at a minimum distance of TDC bin*v (e.g. 3 cm with 200 ps resolution)
hits belonging to the same physical event have the same total charge on the two projections
avalanche charge has a broad distribution, so that different avalanches are unlikely to produce the same charge
This can help to distinguish among hits falling on strips closer than TDC bin*v. This method although probabilistic, can work even with neighboring strips.
1cm
200 ps resolution
100 ps resolution

## Slide 17: Charge based discrimination
The charge matrix:
Locating the real hits only in correspondence of elements compatible with 0.
The charge calibration matrix:
Is the distribution variance calculated on single hits
The condition of compatibility with a real hit
68% fake cut
95.5% efficiency
Overall fakes cut: 89%
Overall efficiency: 95%
…Using a poor time resolution
Saturated and uncalibrated amplifiers
Non optimized CS
Cable length uncertainties….

## Slide 18: The 2d meantimer t0 determination and multiple hits
Determination of the absolute impact time
The absolute impact time is the real time of the avalanche corrected by the hit propagation time
t0ik=
This can be easily calculated once made sure that the hits and are originated by the same event.
allows to associate simultaneous hits
  by knowing the source angle with respect to the chamber surface one can compute the time of the event by correcting for the ToF
Allows precise time stamping of single hits
In case of 2 hits (one readout per strip)
For a signal duration of ~1ns  20cm occupancy on the strip
For an amplifier shaping of 20 ns.
The first hit physically arriving at the FE is measured (could be the farther is has a lower t0 ) and associated correctly
the presence of multiple hits is revealed by the ToT
1ns
5 ns
20 ns

## Slide 19: The 2d meantimer for multiple hits on the same channel
In case of 2 hits
The hit 2y is not timely measured so it can not be paired to an orthogonal strip which we expect to contain an unpaired hit
This can be reconstructed ex post after all the other hits (1,3,4) have been paired
1
2
3
4
Full readout
Having the readout on both end of the strips would solve exactly this problem
This option is available if a very high occupancy is expected
Readout proposal for tracking calorimeters
Can use a very fine pitch  1-2 mm strips
Enables particle flow measurement
2N (or 4N) channels out of the sensitive area

## Slide 20: The ATLAS RPC Muon System today
No RPCs in the inner layer just MDTs
OUTER LAYER for High pT trigger
  One doublet chamber
MIDDLE LAYER for Low pT trigger
  Two doublet chambers
IN TOTAL 6 independent layers measuring Eta and Phi
Hard wired trigger system (on chamber)

## Slide 21: Upgrade of the atlas muon barrel
The trigger chambers in the barrel will undergo a deep upgrade process
The readout and trigger electronics of the present system will be completely replaced for compatibility with the new DAQ system.
Opportunity to implement a new generation of fast TDC in BiCMOS technology
  Rad hard
  Low power consumption
  Time bin of 30 ps without effort
The front end embedded in the chambers is already designed to offer a sharp timing response (narrow band-pass circuit)
NEW chambers will be added to increase the system coverage and redundancy
Will be equipped natively with the new generation front end and TDC
Fully exploiting the potential of the existing ATLAS RPC chambers.
Better time resolution, charge measurement, 2D meantimer

## Slide 22: Trigger detector upgrade proposal: new rpcs
increase the redundancy by adding the RPC inner layer
9 layers instead of 6
4 chambers instead of 3
  This idea was already considered in the original project of the barrel trigger detector, but at that time the need for the 3rd station was not stringent and it was canceled when a substantial downgrade was required to Atlas
BM.CO
BM.PI
BO
BI

## Slide 23: Complete the job: From the bis78 to the bi…

## Slide 24: Impact on physics (just mention, real studies needed)
  Benefits of the extended coverage and the new electronics
  E.g. Channels with a single muon (for example W’)
  Eta distribution is more peaked in the barrel.
  Spatial correlation effect for two muon decays (also holes are very correlated in space).
BO
BI
BM
Bunch crossing
T0
T1
T2
5m
7,2m
9,5m
TOF and possible TOF trigger
  BI RPCs boost the TOF performance:
    Almost doubled lever arm of the active volume
    New gas gaps with 0.4 ns resolution each  ~200pS for a triplet
    Overall 0.5 % of sensitivity o
  based trigger to select slow particles
  5D tracking of the displaced vertex decays

## Slide 25: conclusions
A innovative way of exploiting the RPC features is presented: the 2D meantimer readout
The success of this idea depended critically on the availability of high performance low cost low power consumption and rad hard TDC
This circuits are under development (R. Cardarelli) exploiting the features of BiCMOS SiGe technology
The present and future atlas chambers are fully compatible with this scheme, which would improve the ATLAS discovery potential
An extreme implementation of the 2D meantimer readout of RPCs would allow to simplify the design of a new generation of tracking calorimeters, avoiding the pad readout and the electronics on the sensitive area

## Slide 26: Backup Slides

## Slide 27: search for long lived sleptons and R-hadrons
  Search for heavy  slow charged particles
    Triggered with a single muon or missing transverse momentum
    Selected offline by measuring
    Present ATLAS combined resolution in is 3,5%
    BI RPCs + new electronics on the present system can improve by a factor of ~5 (limited to the barrel…)
    the S/N can be enriched by introducing a trigger on
  Search for displaced vertexes
    The main problem is the pileup and the eventuality that the decay falls in the next BC.
    Under heavy pileup the crucial feature is to label in time the segments to select the hits compatible with a slow track to associate it to the correct BC
    The 2D meantimer system would the ideal tool to boost this type of searches (time resolution + pileup immunity)
CERN-PH-EP-2012-236
arXiv:1211.1597v2 [hep-ex] 25 Mar 2013

## Slide 28: Trigger and detector performance issues
LIMITED COVERAGE
The present barrel coverage is 73%
78% including the feet but not Phase II compliant (just 4 Layers)
ADDITIONAL PERFORMANCE REQUEST
To keep the L1MU20 rate in a reasonable range we need to sharpen the momentum resolution and suppress fakes
RUNNING RPCs BEYOND THE QUAIFICATION LIMITS
10 Years of operation and 300mC/cm^2 at maximum 100 Hz/cm^2
It will be a risk to rely just on the present RPCs for the phase II run
In all cases additional redundancy is recommended…

## Slide 29: Main advantages (anticipation)
Coverage increase (from 73  >96%) closing the holes in the barrel
VERY reliable BCID single layer resolution 0.4 ns (new chambers) 1 ns (old chambers)
Trigger robustness
  Increased redundancy to backup the old chambers
     BI triplet can backup the old RPCs chambers where needed
    Very efficient the new generation of RPCs qualified for very high rate (> 15 kHz/cm2)
  stand alone dedicated system  reliable
  Uniform trigger detector  simpler trigger signal management
Trigger selectivity
  Pileup insensitive due to High space –time RPC granularity ~ 0.5 cm2 x 0.5 ns
  sharper momentum threshold increase of the lever arm
The combination of a new electronics and an additional layer in the inner region will permit to gain several key advantages: