## Slide 1: Study of MRPC simulation performance at BESIII
Fenfen An
anff@ihep.ac.cn
Institute of High Energy Physics, Beijing
2016.02.24
RPC2016@Ghent

## Slide 2: Introduction
BESIII is a general-purpose detector located at the upgraded Beijing Electron-Positron Collider (BEPCII), which runs at -charm physics energy region
The TOF sub-detector, part of the BESIII PID system, its endcap has not so good resolution and fine ability to separate . Improvement is determined to better meet BESIII physics goals
We upgrade the scintillator endcap with MRPC and develop the simulation software using Geant4
The simulation method is introduced and its performance is studied about time resolution and efficiency based on data taken from two test modules
Introduction

## Slide 3
BESIII Collaboration
Introduction

## Slide 4
BESIII is designed cylindrically symmetric around the interaction point, covering 93% of the solid angle
TOF endcap locates between MDC and EMC. It’s upgraded with MRPC, replacing the old scintillator
BESIII Detector
Introduction

## Slide 5
R & D
MRPC prototype
Two testing modules are installed into BESIII and take data
The whole endcap is updated and take data
MRPC
Performance
pre-research
2015 before
2015.01
2016.02
simulation software development and performance study based on test data
hardware
simulation
Tune MC to real data. Guide physics analysis
TOF Endcap Upgrade
Introduction

## Slide 6
Each MRPC module consists of 12 gas gaps (0.22 mm) separated by glass plates (0.4mm)
Signal charge is induced in the readout strips inset in the PCB boards, and is read out on both sides
Working gas: 90% C2F4H2 (R134a), 5% SF6, 5% iso-butane
Simulation Method
MRPC Detector

## Slide 7
Bare chamber built of layers of materials
Placed in an 25 mm thick aluminum frame with FEE boxes
Two layers face-to-face in one endcap to overcome dead areas at the borders
Detector Construction
Simulation Method
Use Geant4 !!!

## Slide 8
Primary ionization characteristics of the working gas are determined by Geant4
  Working gas: 90% + 5% iso-butane + 5%
  Using the energy deposition provided by Geant4, the number of ionized electron-ion pairs in tracking can be calculated, and the uncertainty is considered by smearing a Gaussian function
A primary cluster ~3.6 electron-ion pairs
A average of ~3 clusters in one gap
Primary ionization
Simulation Method

## Slide 9
Electrons from primary ionization are multiplied under electric field. Avalanche development exclusively depends on the field intensity E.
The probability to get secondarily ionized and attached are characterized by Townsend () and attachment () coefficients.
The avalanche speed is characterized by drift velocity
Simulation results from MAGBOLTZ for our working gas under standard temperature and pressure
Electron Multiplication
Simulation Method

## Slide 10
Avalanche process is simulated based on the 1D-model introduced in Ref. [Nucl. Instrum. Meth. A 500 1-3]
1. Each gas gap is divided into N steps of size dx
2. Primary electron-ion pairs distribution along
the gap is provided by Geant4
3. The number of electrons at distance
x+dx is calculated according to the predicted
probability
4. Repeat step 3 until all electrons have left the gap
Saturation effect is considered by applying a simple cut-off at . It is satisfactory because the main characteristics such as efficiency and resolution are only sensitive to the early stage of an avalanche
Electron Multiplication
Simulation Method

## Slide 11
𝑖(𝑡)=𝐸_𝑤𝑒𝑖𝑔ℎ𝑡 𝑣_𝑑𝑟𝑖𝑓𝑡 𝑄_𝑒 𝑁(𝑡)
electronic charge
Weighting field
Drift velocity
the number of electrons in an avalanche at time
the number of electrons in an avalanche at time 𝑡
electronic charge
Weighting field
Drift velocity
Signal current is induced on the strips by the electron movement in the electric field, which can be calculated by Ramo’s theorem
[S. Ramo, Proceedings if IRE 27 (1939)]
Charge spectra in different electric fields
The left peak is caused by hits at the chamber borders or under the strip intervals
7000 V HV is applied by the BESIII experiment, resulting in a signal peak around 1 pC
Charge Induction
Simulation Method

## Slide 12
Threshold crossing time : time when induced charge exceeds
vs Charge
projection
jitter vs Charge
Propagation time : time propagating along the strips, assuming a propagation speed of 0.8
Charge-Time Conversion
Simulation Method

## Slide 13
Time over threshold TOT: converted from the charge spectrum
TOT jitter vs Charge
TOT projection
Charge to TOT conversion
Charge-Time Conversion
Simulation Method

## Slide 14
We simulate Bhabha events with electric field E and charge threshold set at different values and reconstruct the time following the same way as when dealing with real data.
Two testing MRPC modules have participated
in taking physics collision data under such
working points:
  Seven high voltages (V): 6700, 6850, 7000,
  7150, 7300, 7450
  Four thresholds (mV): 110, 150, 200, 250
  The behavior of detection efficiency and time resolution with E and is studied and compared with experimental data
Two testing modules are installed, replacing the old scintillator
Performance Study
Performance Study

## Slide 15
Time reconstruction method:
  MDC tracks is extrapolated to determine
  the impact position
  Signal is searched for in the matched and
  neighbor strips
  Measured time is calculated
Character variables
MC and data reconstruction follow the same way, except that the correction item is different
Time difference:
Measured time of flight
Expected time of flight
  Detection efficiency:
Time Reconstruction
Performance Study

## Slide 16
A comparison between data and MC at:
E=7000 V, =400 fC
57ps includes:
Jitters depending on charge; TDC: 25ps;
Arising from 12 gaps: 10ps; Electronics: 20ps;
Others: 15 ps
: resolution of distribution
Time resolution ~ HV
Time resolution ~ threshold
Time Resolution
Performance Study

## Slide 17
, ratio of the number of good signals over that of extrapolated MDC tracks
is required to be less than 0.8 ns to suppress backgrounds
MC efficiency plateau around 97%. The 3% loss is due to event start time determination, limited signal search area …
Detection efficiency ~ HV
Detection efficiency ~ threshold
Detection Efficiency
Performance Study

## Slide 18
Simulation software is developed for the new MRPC detector at BESIII
Simulation method is introduced
Simulation performance with HV and threshold is studied. Data points taken by testing modules are also plotted for comparison
More precise tuning will be done based on the future collision data. Put into use for data analysis
Thank You
Summary & Outlook
Summary & Outlook