## Slide 1
Marcello Abbrescia
Dipartmento Interateneo di Fisica
University of Bari
Improving
rate capability of
Resistive Plate Chambers

## Slide 2
Let us start from…
… one of prof. Santonico’s presentations:
(Second ECFA workshop on HL-LHC, Aix-les-Bains, 21-23 Oct. 2014)
In the static limit the voltage applied to the chamber Δ Vappl is entirerly transferred to the gas; but, for a working current i, part of this voltage is needed to drive the current in the electrodes
Δ Vgap= Δ Vappl – RI = Δ Vappl - Δ Vel
With Φ =counts/surf. the voltage transferred to the electrodes can be written as:
Δ Vel = ρ d Φ <Q>
“A high rate requires to keep
Δ Vel at a negligible value wrt.
Δ Vgap even under heavy irradiation”
Electrode resistivity
Electrode total thickness
Charge/count

## Slide 3
Let us start from…
Essentially the same approach used in:
G. Carboni et al. A model for RPC detectors operated at high rate, NIM A 498(2003), 135-142
“ The current drawn by a detector exposed to a particle flux Φ (particles/s) is:
I = Φ q = Φ G qi
where qi is the ionization charge and G is the gain.”
“In a given detector the electric field, the gain and the current are uniquely determined by
Δ Vgap, where
Δ Vgap = V0 – IR
And R is the total electrode resistance, given by:
Basically the application of the Ohm’s law

## Slide 4
What we learn from that formula
It is a first (rough) approximation of complex processes.
At first order:
  Electrode resistivity does influence rate capability;
  Electrode thickness does influence rate capability;
  Gap thickness does not seem to play any role.
There is not a direct way to compute which is the effect of a reduction on ΔVel= Δ Vappl - Δ Vgap on the rate capability.
Bakelite thickness can account for a 25-50% reduction on Δ Vel
  (Ex. from 21.5-1 mm)
Bakelite resistivity can account a 10 (or more) factor on Δ Vel
(Ex. From 5 × 1010  5 × 109 Ωcm)
 Electrode thickness seems to play a second order role.
ΔVel = ρ d Φ <Q>
Later on…

## Slide 5
Let us use something more elaborate
Exponential growth
Saturation
Exponential growth
xsat
Saturation
“Drift”

Note that most of the variables here are stochastic variables (qind is the convolution off all these probability distributions), so it is
not immediate to get analytical results…

## Slide 6
HV=9.2 kV
Simulation
Experiment
HV=9.5 kV
Simulation
Experiment
HV=9.7 kV
Simulation
Experiment
HV=10.1 kV
Simulation
Experiment
Experimental data from Camarri et al., NIM A 414 (1998) 317-324
Gas mixture:
C2H2F4/C4H10 97/3 + SF6 2%
Input for simulation: Colucci et al., NIM A 425 (1999) 84-91
Quite a successful model...
This is not a fit!
“Saturation” peak
“Inefficiency”peak

## Slide 7
Let us move to a dynamic model


Cg
Rb
Cb
A few numbers:
typical avalanche radius: 100 m
typical avalanche charge: 1 pC
typical external charge contained in 100 m: 10 pC

Time constant τ depending only on material characteristics and not on “cell” dimensions
Also capacitive effects taken into account

## Slide 8
And what REALLY happens…
Applied HV
=1500 ms
Cell area = 1 mm2
  5  10 11 cm
=20 Hz
We assume that the voltage on the electrodes goes back to HVappl following an exponetial law
Note that “big” pulses come only after that HVappl has been restored, and they are followed by “small” pulses
Complex “feedback” mechanisms…
Average HVgap value of the “static” model

## Slide 9
Applied HV
10 Hz
13 Hz
20 Hz
The effective HV diminishes and its distribution is broader.
Two consequences:
lower HV at high rate
greater HV variations at high rate
Some of the differences
Reduction off the effective HV correctly foreseen by the static (ohmic) model)
Spread of the effective HV not foreseen at all
Average HVgap of the “static” model

## Slide 10
Efficiency: comparison with data
Data from G. Aielli et al., NIM A 478(2002) 271-276
Simulation
Experimental
~ 1.5 kHz/cm2
~ 2 Hz/cm2
Note that there also exists an approximated formula for efficiency:
Basic aspects reproduced:
Plateau efficiency reduced at high rate
Shift of the efficiency curves
Change in slope of the efficiency curves
Not so immediate (if possible) to reproduce the same effect with the static model

## Slide 11
Rate capability dependances
 4  1011 cm
 8  1010 cm
 1011 cm
HV=10100 V
 6  1011 cm
Exp. streamer
Exp. avalanche
Simulation
streamer
 8  1010 cm
Electrode resistivity
Charge contained in the discharge
“High” resistivity
“Low” resistivity
“High” charge
“Low” charge
Data from R. Arnaldi et al., NIM A 456(2000) 73-76
Here we find the other important aspect related to the charge travelling in the gap and the importance to reduce it
  But this implies a signal reduction as well!

## Slide 12
About gap thickness:
The trick to increase rate capability is to increase qind keeping Qgap constant, while
ηg stays (roughly)constant.
Qgap
ng= number of gaps
1
0
0
0
Saturation term

## Slide 13
About gap thickness:
The point is that if you reduce the gap thickness only the shielding electrostatic effect of the bakelite plates increases in proportion
  qind is reduced (keeping Qgap constant)
  Rate capabity is reduced
The voltage drop in the gap related to the weighting field should be as high as possible
If you reduce the electrode thickness at the same time, the two effects cancel out
Experimental data show that wider gaps show higher rate capability
(also for other reasons)
It would be “strange” that the 2 mm gap is the minimum
Efficiency
1
1
0
0

## Slide 14
Time resolution in an RPC
What is the origin of signal time fluctuations in an RPC?
There are very good analytic studies (Mangiarotti et al.),
here just a few hints will be given from a MC point of view.
All the cluster in the gap contribute at the same manner to the signal
Fluctuation are not (directly) related to the particle transit time in the gas gap
Total number of clusters
Total number of electrons in each cluster
Fluctuations superimposed on the exponential growth
Present at low rate
Only present at high rate
Fluctuations of η
Fluctuations of vd

## Slide 15
Time resolution at high rate
Data from C. Bacci et al., NIM A 352(1995) 552-556
0.2 kHz/cm2
=0.9 ns
1 kHz/cm2
=1.2 ns
4 kHz/cm2
=1.6 ns
Simulated
Experimental
General behaviour well reproduced ...
Simulated time resolutions slightly less than experimental
“Instrumental” effects not included
Note that all these aspects related to time resolution cannot be accounted for in the static model

## Slide 16
The avalanche charge arriving on the electrodes surfaces spreads more or less depending on ration between surface resistivity ρsur and volume resistivity ρvol
It has a direct influence on the amount of voltage drop in the gap
“large”
“small”
avalanche
“Surface” coupling resistors
Cg
Rb
Cb
Rs,b

The result is that the current flows not only in the “central” cell, but also in the neighbouring ones.
  The time constant depends on the two parameters ρvol AND ρsur
Reality is more complex…

## Slide 17
(Some) Conclusions
The static model used in many discussions
(presentations) is a first order approximation of what happens
  Like putting a straight line where a complex phenomenon is happening
  Assumes a purely resistive behaviour while capacitive effects can be predominant
Clear dependances of rate capability on some constructive parameters are clearly spotted in a more complete view
  Resistivity, charge, electrode thickness
  All this should be considered in current R&D
Amazingly, the most complete and interesting view is still to be thoroughly investigated
More calculations and considerations are welcome!